TDDS

First things first, you must have an odd number of points in all directions in order for the DAF to work.
Secondly the Quantum proton must be in the center of the grid to start.

IOp's for TDDS

These Iop's are specifically for running TDDS to achieve a high level of theory PES.
-This means two things
1.The Nuclei are not propagated
2. The potential surface should converge after a few iterative time steps
1/33- Junjie Debug print

1/73- Initial Kinetic energy of the nuclei.
- This formalism uses N*Microhartree
- Where N is the value input into the IOp
- In order to solve for the temperature you can use E= (# of dimensions) *KT
-Here K is the boltzmann constant
1/8- ADMP time step
=0 this is the default setting (0.1 femtosecond)
=N where N is really N*0.0001 fs
- N=5 means 0.0005 fs
2/15- Symmetry control
-In this case n=3, which means that symmetry is not even called
-This is a gaussian standard Iop

1/179,1/178,1/177 → X directional cosines
1/176,1/175,1/174 → Y directional cosines
1/173,1/172,1/171 → Z directional cosines
→ These values describe the alpha, beta, and gamma values that are associated with describing the coordinate system of the grid
→ N*0.000001 gives the actual value of the direction cosine

1/193=XY → grid option
    Y=1 → moving grid
Y=2 → Fixed grid

1/190 =N where N is the dimensionality of the grid

1/186=WWXXYYZZ
XX → atom at the origin of the grid
YY → atom at the end of the grid
ZZ → Quantum Atom
WW → Optional Flag

1/194 → the integration scheme used to interpolate the PES from point to point
 =0 Haar wavelet decomposition is used
=1 Marginal Sampling is used

1/170=ZZZYYYXXX
→ the number of quantum grid points in each direction

1/169=ZZZYYYXXX
→ grid spread in 10^2 A

1/184 =NZZZYYYXXX
→ The number of regular grid points in each direction
→ N is the interpolation flag

1/180 → grid cutoff QW propagation in 10^-5 A
→ if the distance between two atoms is below the set value the potential is extrapolated or	skipped

1/187 → Number of full quantum wavepacket dynamic steps per ADMP step

1/189=NXXYYYY
→ YYYY is the temperature
→ XX is IrdChi
→ N is a flag
→ The sign of the Iop is the sign of the temperature
→ if N=0 the temp is set by the Nuclear kinetic energy

1/195 → JYY
→ Information for wavelet decomposition

1/188 =NXXYY
→ YY the number of Krylov basis vectors used in the Arnoldi Diagonalization
→ XX then umber of eigenvectors to be calculated
→ N the number of times the matrix will be diagonalized